## Slide 1
Networking Infrastructure
Routing Protocols
Lecture
NI
3
Networking Infrastructure
Diploma in CSF / IT
Year 2 (2020/21), Semester 3
Notes: Left-hand Bar – Replace FSP by your module code and X by the lecture number.
Replace Lecture Title
Replace < Module Name >
Replace Year and Semester if necessary

## Slide 2: Routing In A Network
Objectives
Recap the functions and benefits of routers
Describe static routing
Understand the concept of Static routing
Ability to configure Static routing
Notes: https://www.routeralley.com/guides/static_dynamic_routing.pdf

## Slide 3: Functions Of A Router - Recap
A router is a multi-port internetworking device that interconnects two or more networks. It performs “forwarding and filtering” of data packets between these networks at the network layer.
A router makes decisions based on the destination IP address of a packet unlike a switch that uses a MAC address in a data frame to perform switching.
A router routes packets from one network to another network until it reaches its destination based on the destination IP address.
Notes: A switch performs “forwarding and filtering” of data frames between LAN segments at the Data Link (MAC) layer.

## Slide 4: Functions Of A Router - Recap
Routing Table | 
Network Address | Outgoing Interface
153.20.0.0 | P1
192.168.1.0 | P2
210.1.1.0 | P3
153.20.0.3
255.255.0.0
153.20.0.4
255.255.0.0
192.168.1.2
255.255.255.0
192.168.1.3
255.255.255.0
192.168.1.4
255.255.255.0
210.1.1.2
255.255.255.0
210.1.1.3
255.255.255.0
210.1.1.4
255.255.255.0
192.168.1.0
153.20.0.0
210.1.1.0
153.20.0.2
255.255.0.0
R1
P1
P2
P3
192.168.1.1
210.1.1.1
153.20.0.1
Switch 1
Switch 2
Switch 3
Notes: Outgoing Interface on Cisco Router: G0/0, G0/1 (or Fa0/0, FA0/1)

## Slide 5: Network ID - Recap
The router is connected to three networks. The networks IDs are 153.20.0.0, 192.168.1.0 and 210.1.1.0 respectively.
Each network device needs to be configured with IP address and subnet mask
IP address has two components: network and host.
Subnet mask extracts the network component from an IP address
For example, a PC with IP address 192.168.1.1 and subnet mask 255.255.255.0, the Network ID is 192.168.1.0
A router keeps track of Network IDs and not every individual IP address.

## Slide 6: Benefits Of A Router
Separates network logically into subnets; reduces network traffic as packets are only routed to their destination subnet
Isolates MAC broadcasts as it does not forward broadcast frames.
Connects different protocols: LAN protocols (e.g. Ethernet MAC) and WAN protocols (e.g. PPP).

## Slide 7
Routing in Action - Recap
NW 1: 153.20.0.0
NW 2: 75.0.0.0
NW 3: 200.30.10.0
NW 4: 133.33.0.0
NW 5: 222.20.2.0
153.20.88.99
133.33.3.3
R1
Notes: Refer to OSNF 2019 – Week 16 Lecture.

## Slide 8: Activity – Functions & Benefits of Routers
Complete Tutorial
  Activity 1, Q1 to Q5
  Activity 2, Q1 to Q4

## Slide 9: Static Routing
Static routes are entries in the routing table of the router that are manually configured (user-defined fixed path entries)
Administrator must know the entire network and manually configure all routes if all routes are static
Useful in a stub network (a network that is only accessible by one path)
Image source: http://i.stack.imgur.com/7wphw.gif access on 27 Sep 2016

## Slide 10: Static Routing – Stub Network
http://image.slidesharecdn.com/day81introducingrouting-150514063503-lva1-app6892/95/day-8-1-introducing-routing-9-638.jpg?cb=1431587930
Notes: A stub network is a computer network, or part of an internetwork that send all of its non-local traffic out via a single path, with the network aware only of a default route to non-local destinations.
Since the stub network is connected to a single path to the rest of the internet, the router of the stub network can only send to one router, so it does not need to know any other route information. So a static route pointing to the default route is the most efficient way to configure the router.

## Slide 11: Static Routing – Stub Network
http://http://www.learncisco.net/assets/images/icnd1/91-static-route-example.jpg

## Slide 12: Benefits of Static Routing
Enhance Security
  Administrator might want to hide parts of an internetwork and specify only those parts that need to be revealed; dynamic routing tends to reveal everything known of an internetwork
  Static route force traffic to take a specific, secure route instead of a route determined dynamically which can change as the network topology changes making traffic travel over an insecure route
Does not consume much traffic as no routing updates are transmitted

## Slide 13: Bad thing about Static Routes
Not suitable for large networks as administrator must know the entire network and manually configure all routes if all routes are static
Any change to the network means re-configuring all routers to reflect the change
Not be able to re-route the traffic if a link fails

## Slide 14: Activity – Concepts of Static Routing
Complete Tutorial
  Activity 1, Q6 to Q9
  Activity 3, Q1

## Slide 15: Static Route Operation
Three-part sequence
Network administrator configures the route in the router
The router installs the route in its routing table
Packets are forwarded based on the static route entries in the routing table

## Slide 16: Static Routing

## Slide 17: IP Route Command
There are two ways to define a static route using the “ip route” command
Specifying the outgoing interface for the packet
  Only possible for Point-to-Point connections
Specifying the Next Hop IP address for the packet
  Works for all types of connections

## Slide 18: Specifying Outgoing Interface

## Slide 19: Specifying Next-Hop Address

## Slide 20: Example
What is the command to set up a static route on router “sterling” for the 172.16.5.0 network on the Ethernet LAN of router “waycross”?
Sterling(config)#ip route 172.16.5.0 255.255.255.0 172.16.2.2
Destination Network
Subnet mask
Next-hop address

## Slide 21: Default Route
A default route is a special static route that uses this format:
Default routes are used to route packets with destinations that do not match any of the other routes in the routing table.
Routers are typically configured with a default route for Internet-bound traffic since it is often impractical and unnecessary to maintain routes to all networks in the Internet.
Only one route out
Notes: Default route - also known as the gateway of last resort, is the network route used by a router when no other known route exists for a given IP packet's destination address. All the packets for destinations not known by the router's routing table are sent to the default route.

## Slide 22: Verifying Static Route Configuration
The command show running-config is used to view the active configuration in RAM to verify that the static route was entered correctly.
The show ip route command is used to make sure that the static route is present in the routing table

## Slide 23: The show ip route Command
sterling#sh ip route
Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
S 172.16.5.0/24 [1/0] via 172.16.2.2
C 172.16.1.0/24 is directly connected, FastEthernet0/0
C 172.16.2.0/24 is directly connected, Serial2/0
Note: Administrative Distance is just a number (0 to 255) set by Cisco to indicate the reliability of the route (0 is most reliable). For static route, the default admin distance is 1. Metric for static route is always 0 because the next hop router is 0 hop away.
S 172.16.5.0/24 [1/0] via 172.16.2.2
Destination Network
Administrative Distance/Metric
Next Hop Address

## Slide 24: The traceroute command
The packet is able to reach 172.16.4.2 but gets no response after that. Possible causes include:
The destination’s firewall or other security device is blocking the request.
There could be a problem on the return path from the target system..
Diagnostic tool for displaying the route (path) and measuring transit delays of packets across an Internet Protocol (IP) network.
Notes: The destination’s firewall or other security device is blocking the request. •There could be a problem on the return path from the target system. Remember the round trip time measures the time it takes for a packet to travel from your system to a destination system and back. The forward route and the return route often follow different paths. If there is a problem on the return route, it may not be evident in the command output. •There may be a connection problem at that particular system or the next system.

## Slide 25: Routing In The IP Environment
Summary
Static routes are manually configured routes
Good for small networks, not good for large networks
Good for security
Notes: https://www.routeralley.com/guides/static_dynamic_routing.pdf

## Slide 26: Activity – Concepts of Static Routing
Complete
  Practical
  Tutorial Activity 3, Q2