## Slide 1
Networking Infrastructure
Dynamic Routing Protocols
Lecture
NI
4
Networking Infrastructure
Diploma in CSF / IT
Year 2 (2020/21), Semester 3
Notes: Left-hand Bar – Replace FSP by your module code and X by the lecture number.
Replace Lecture Title
Replace < Module Name >
Replace Year and Semester if necessary

## Slide 2: Dynamic Routing
Objectives
Explain the fundamentals of dynamic routing
Explain the routing information protocol (RIP) and OSPF
Understand the difference between Distance Vector Protocols (RIP) and Link State Protocols (OSPF)
Explain the advantages of dynamic routing over static routing
Configure dynamic routing protocol – RIP

## Slide 3: Basics of Dynamic Routing
Two key dynamic routing protocols are Routing Information Protocol (RIP) and Open Shortest Path First (OSPF)
Dynamic routing protocols can be classified as distance vector (used by RIP) and link state (used by OSPF)

## Slide 4: Basics of Dynamic Routing
Minimum configuration and set-up is required
Routes are automatically discovered and maintained by routers through the exchange of routing information between them
Routing decisions are made based on dynamically learned routes

## Slide 5: Distance Vector Protocol
Each router informs its neighbours of its entire routing table periodically
Routing information that is sent to its neighbours routers consists of destinations (vector) and costs (how far is the path to the destination?) and the next hop to get there
Router selects the neighbour advertising the lowest cost (least number of hops)
If router A learns that its neighbour, router B can get to router D in two hops, the router can assume that the path from itself to router D is three hops

## Slide 6: Dynamic Routing Activity
Network | Next Hop | Cost
Network | Next Hop | Cost
Network | Next Hop | Cost
Network | Next Hop | Cost
Notes: Form 4 groups, each group is assigned a router
Each group will write on a piece of paper the routing table containing Destination Network, Next Hop Router, Cost (Number of hops) and Update#
Initial configuration – fill in the Network connected to each interface of the group’s router in the routing table
Update# 1 - each group will share their current table with their adjacent routers only. New Networks and Routers learnt on the first round, Update# is 1
Update# 2 - each group will share their current table with their adjacent routers only. New networks learnt on the second round, Update# is 2. For 2 routes to the same network, keep the route with the smaller update#.
Note: update process will repeat till every router knows every network.
What happens when 1 of the routes is broken?

## Slide 7: Distance Vector Protocol - Initial
Network | Next Hop | Cost
A | Direct | 0
B | Direct | 0
E | Direct | 0
Network | Next Hop | Cost
B | Direct | 0
C | Direct | 0
Network | Next Hop | Cost
C | Direct | 0
D | Direct | 0
F | Direct | 0
Network | Next Hop | Cost
E | Direct | 0
F | Direct | 0

## Slide 8: Distance Vector Protocol - Update 1
Network | Next Hop | Cost
A | Direct | 0
B | Direct | 0
E | Direct | 0
C | Router B | 1
F | Router D | 1
Network | Next Hop | Cost
B | Direct | 0
C | Direct | 0
A | Router A | 1
E | Router A | 1
D | Router C | 1
F | Router C | 1
Network | Next Hop | Cost
C | Direct | 0
D | Direct | 0
F | Direct | 0
B | Router B | 1
E | Router D | 1
Network | Next Hop | Cost
E | Direct | 0
F | Direct | 0
A | Router A | 1
B | Router A | 1
C | Router C | 1
D | Router C | 1

## Slide 9: Distance Vector Protocol - Update 2
Network | Next Hop | Cost
A | Direct | 0
B | Direct | 0
E | Direct | 0
C | Router B | 1
F | Router D | 1
D | Router B | 2
Network | Next Hop | Cost
B | Direct | 0
C | Direct | 0
A | Router A | 1
E | Router A | 1
D | Router C | 1
F | Router C | 1
Network | Next Hop | Cost
C | Direct | 0
D | Direct | 0
F | Direct | 0
B | Router B | 1
E | Router D | 1
A | Router B | 2
Network | Next Hop | Cost
E | Direct | 0
F | Direct | 0
A | Router A | 1
B | Router A | 1
C | Router C | 1
D | Router C | 1

## Slide 10: Distance Vector Protocol
Routers send out their own routing information to its neighbouring routers
Within a few minutes, all the routers would have exchanged the updated information and have a view of the network including all the routes
When all routers have a full view of the network the network is said to have “converged”

## Slide 11: Distance Vector Protocol - RIP
Routing Information Protocol
Uses hop count as its routing metric to determine the shortest route to the destination router
Does not take into consideration the speed, delay, and reliability
Maximum number of hops is 15
A route with a hop count of 16 is flagged as unreachable
Update its routing table to neighbours every 30 seconds. Generate a lot of overhead traffic
Notes: Hop Count does not take into consideration the speed, load, reliability, or latency(delay) of any particular hop, but merely the total count.
Uses Bellman-Ford algorithm to determine the shortest path

## Slide 12: router and network Commands

## Slide 13: Basic RIP Commands
Using router rip and network commands to Enable RIP on an IP-addressed network
Monitoring IP packet flow using the show ip protocol command
The show ip route command

## Slide 14: The Configuring RIP command

## Slide 15: The show ip protocols command

## Slide 16: Sample Routed Network

## Slide 17: The show ip route command
Sterling#sh ip route
Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP
D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area
* - candidate default, U - per-user static route, o - ODR
P - periodic downloaded static route
Gateway of last resort is not set
172.16.0.0/16 is subnetted, 5 subnets
C 172.16.1.0/24 is directly connected, FastEthernet0/0
C 172.16.2.0/24 is directly connected, Serial2/0
R 172.16.3.0/24 [120/1] via 172.16.2.2, Serial2/0
R 172.16.4.0/24 [120/1] via 172.16.2.2, Serial2/0
R 172.16.5.0/24 [120/2] via 172.16.2.2, Serial2/0
Note: Admin Distance for RIP is 120. 172.15.5.0 network is 2 hop counts away

## Slide 18: Link State Protocol
A link state router will first discover who their neighbouring routers are and then start to exchange packets called Link State packets (LSP).
LSP contains information (state, attached interfaces, metrics) about the networks the router is directly connected to.
Require routers to send only updates (not entire routing table) to other routers when there are changes.
Compared with distance-vector:
  Less bandwidth-intensive
  Faster convergence time (react quickly to topology changes)
  More CPU and memory resources required
Notes: RIP vs OSPF: https://techdifferences.com/difference-between-rip-and-ospf.html

## Slide 19: Link State Protocol - OSPF
Open Shortest Path First (OSPF) is a Link State Protocol
Uses a metric called cost to calculate optimal route to destination network. This cost metric is based on a variety of factors such as speed, reliability and delay.
A metric is a variable assigned to routes as a means of ranking them from most preferred to least preferred (hop count is a metric used by RIP)

## Slide 20: Link State Protocol - OSPF
Factors used for calculating cost metric (routing metric):
  Speed – refers to the speed of each link. Higher speed links have a lower cost than low speed links.
  Delay – refers to the length of time required to move a packet from source to destination through the internetwork.
  Reliability – refers to the dependability (usually described in terms of the bit-error rate) of each network link. Reliability of links in developed countries is usually higher than developing countries.
Notes: Some of the factors used for calculating a routing metric are as follows: speed, reliability or latency(delay).
A full list of factors:
•Hop count (used by RIP)
•Path speed
•Path reliability
•Latency (delay)
•Load
•Bandwidth
•Maximum transmission unit

## Slide 21: Link State Protocol - OSPF
Router A’s Routing Table
Notes: Note the error in the Router A’s Routing Table: Network C can be reached via Router D with cost of 9, i.e. preferred over via Router B with cost of 10.

## Slide 22
OSPF Default Cost

## Slide 23: Benefits of Dynamic Routing
Simpler to configure routers on large networks
Routes are automatically discovered and maintained by routers, reducing administrative effort
Router can respond automatically to topology changes such as new or deleted routes
Automatic re-routes enable network to be resilient