## Slide 1
Firewall Technologies
LECTURE
NS
Diploma in CSF
Year 3 (2021/22), Semester 5
Network Security
2

## Slide 2: Objectives
At the end of this, you will get to know more about firewalls:
Types of Firewalls
Firewall Deployment Options
Virtual Wire Interface
Layer 3 Interface
  Security Zone
  Interface Management Profile
  DHCP
  Virtual Router

## Slide 3: Type of Firewalls
Packet Filter Firewall
Circuit Level Gateways
Application Level Gateways
Stateful Multilayer Firewall
Next-Generation Firewall

## Slide 4: 1. Packet Filter Firewall
The Packet Filtering Firewall is one of the most basic firewalls.
Each packet passing through is inspected and then the firewall decides to pass it or not.
The packet filtering can be divided into two parts:
  Stateless packet filtering.
    If the information about the passing packets is not remembered by the firewall, then this type of filtering is called stateless packet filtering.
    The allow/deny decisions are taken on packet by packet basis and these are not related to the previous allowed/denied packets.
  Stateful packet filtering.
    If the firewall remembers the information about the previously passed packets, then that type of filtering is stateful packet filtering.
    These can be termed as smart firewalls.

## Slide 5: 1. Packet Filter Firewall
Advantage:
The biggest advantage of Packet Filtering Firewalls is cost and lower resource usage and best suited for smaller networks.
Disadvantage:
Packet Filtering Firewalls can work only on the Network Layer and these Firewalls do not support complex rule based models. And it’s also vulnerable to Spoofing in some cases.

## Slide 6: 2. Circuit Level Gateways
Circuit level gateways:
work at the session layer and monitor TCP handshaking between packets to determine whether a requested session is legitimate

## Slide 7: 2. Circuit Level Gateways
Advantage:
Circuit level gateways are comparatively inexpensive
Disadvantage:
Circuit level Gateways do not filter Individual Packets. After Establishing a Connection, an Attacker may take advantage of this.

## Slide 8: 3. Application Level Gateways
Application level gateways
work on the Application layer of the OSI model and provide protection for a specific Application Layer Protocols.
Proxy server is the best example of Application Level Gateways Firewalls, it can prevent any direct connection between a trusted server or client and an untrusted host.
Application level gateway would work only for the protocols which are configured. For example, if we install a web proxy based Firewall than it will only allow HTTP Protocol Data.

## Slide 9: 4. Stateful Multilayer Firewall
Stateful multilayer inspection firewalls
work at the application , session, network layer.
  They filter packets at the network layer, determine whether session packets are legitimate and evaluate contents of packets at the application layer
They allow direct connection between client and host, alleviating the problem caused by the lack of transparency of application level gateways.

## Slide 10: 5. Next Generation Firewall
NGFWs act as a platform for network security policy enforcement and network traffic inspection.
Standard capabilities of the first-generation firewall: This includes packet filtering, stateful protocol inspection, network-address translation (NAT), VPN connectivity, etc.
Truly integrated intrusion prevention: this includes support for both vulnerability-facing and threat-facing signatures, and suggesting rules (or taking action) based on IPS activity. The sum of these two functions collaborating via the NGFW is greater than the individual parts.

## Slide 11: 5. Next Generation Firewall
Full stack visibility and application identification: ability to enforce policy at the application layer independently from port and protocol.
Extra-firewall intelligence: ability to take information from external sources and make improved decisions. Examples include creating blacklists or whitelists and being able to map traffic to users and groups using active directory.
Adaptability to the modern threat landscape: support upgrade paths for integration of new information feeds and new techniques to address future threats.
In-line support with minimum performance degradation or disruption to network operations.

## Slide 12: Palo Alto NGFW Hardware Platforms
PA-3000 Series
PA-2000 Series
PA-4000 Series
PA-5000 Series
PA-500
PA-200
VM- Series
(Virtual Machines)

## Slide 13: Palo Alto Networks Single-Pass Architecture
Single pass:
  Operations per packet:
    Traffic classification with App-ID technology
    User/group mapping
    Content scanning – threats, URLs, confidential data
  One single policy (per type)
  Parallel processing:
  Function-specific parallel processing hardware engines
  Separate data/control planes

## Slide 14: Single Pass Architecture Engines
App-ID™
Identify the application
Content-ID™
Scan the content
User-ID™
Identify the user

## Slide 15: Deployment Options
Virtual Wire Mode
Application ID, Content ID, User ID, SSL Decryption
Includes NAT capability
  Virtual Wire Mode: Using virtual wire interfaces the firewall can be inserted into an existing topology without requiring any reallocation of network addresses or redesign on the network topology.
  In this mode, all of the protection and decryption features of the device can be used.
  NAT functionality is provided in this mode.

## Slide 16: Deployment Options
Layer 3 Mode
All of the Virtual Wire Mode capabilities with the addition of Layer 3 services: Virtual Routers, VPN and, Routing Protocols
  Layer 3 Mode: Using Layer 3 interfaces the firewall can take the place of any current enterprise firewall deployment.

## Slide 17: Ethernet Interface Configuration
Network > Interfaces > Ethernet
Interface Type:
Tap
Virtual Wire
Layer 2
Layer 3
Layer 2
Layer 3
Virtual Wire

## Slide 18: Virtual Wire Interface
Binds TWO firewall interfaces together through Virtual Wire object
Typically used when no switching or routing is needed
No configuration changes for adjacent network devices
  Possible to insert the firewall into an existing topology without requiring any reallocation of network addresses or redesign on the network topology.
Firewall
Virtual Wire object
Virtual Wire interface
No IP or MAC
Virtual Wire interface
No IP or MAC
Zone B
(Virtual Wire)
Zone A
(Virtual Wire)
Traffic inspection and control

## Slide 19: Virtual Wire Interface
Network traffic flows through a firewall in a virtual wire, which means that the firewall can examine traffic and block traffic.
LAN
(User Network)
Internet
E1/2
E1/1

## Slide 20: Configuring a Virtual Wire Object
Network > Virtual Wires > Add
Interfaces in the virtual wire

## Slide 21: Configuring Virtual Wire Interfaces
Network > Interfaces > Ethernet
Security Zone
Virtual Wire Object
Interface Type
Notes: If the virtual wire object has not been configured, the Virtual Wire field can be left blank. The interface names can be specified when the virtual wire object is created.
Since traffic will flow between virtual wire interfaces, a zone is required. Only zones that match the Interface type will be presented by the pull-down in the interface.

## Slide 22: Layer 3 Interfaces
Enables routing between multiple interfaces:
  Requires a virtual router
Requires network configuration to accommodate new IP addresses
Routing between Layer 3 interfaces requires a router. An internal virtual router provides a routable connection between the Layer 3 interfaces.
Firewall
Layer 3 interface
IP address
Layer 3 interface
IP address
Zone B
(Layer 3)
Zone A
(Layer 3)
Traffic inspection and control
Virtual Router

## Slide 23: Layer 3 Interfaces
Internet
E1/3
E1/4
172.16.2.1/24
Routing between networks
Layer 3
10.1.2.1/24
Users
DMZ
E1/5
192.168.2.1/24
Network traffic can flow through a firewall between Layer 3 interfaces, which means that the firewall can examine traffic and block traffic.

## Slide 24: Configuring a Layer 3 Interface
Network > Interfaces > Ethernet
Security Zone
Interface Type: Layer 3
Virtual Router
Click Network > Network Profiles > Interface Mgmt to define a interface management profile
IP Address
Minimum
Requirement

## Slide 25: Configuring Security Zones
Network > Zones
Zone Types:
Tap
Virtual Wire
Layer 2
Layer 3
* multi-virtual system capable firewalls only
Notes: Security zones are defined by type. The available types are:
  Tap
  Virtual Wire
  Layer 2
  Layer 3

## Slide 26: Interface Management Profile
Defines which management functions are allowed on a traffic interface
Management Profiles are applied to Layer 3 Interface(s)
Network > Network Profiles > Interface Mgmt > Add
Restricts administrative access to specific IP addresses
Notes: By default, any management traffic sent to or from the firewall goes through the out-of-band management interface (MGT). Alternatively, a Layer 3 interface can be used to source this traffic and also receive inbound management traffic.
Management features enabled by the profile can be restricted to specific IP address with the Permitted IP Addresses panel. If configured, only the IP addresses listed can use the services selected when defining the profile. If the field is left blank, the profile allows any IP address to used the configured services.

## Slide 27: DHCP Server
Network > DHCP > DHCP Server

## Slide 28: Virtual Routers
Network > Virtual Routers

## Slide 29: Virtual Routers
Virtual routers enable the firewall to route packets at Layer 3 by making packet forwarding decisions according to the destination IP address (IPv4 or IPv6).
Each Layer 3 interface and VLAN interface defined on the firewall should be associated with a virtual router.
When you add an interface, its connected networks automatically are added to the virtual router’s route table and can be used by the virtual router to forward traffic.

## Slide 30: Virtual Router Static Routes
Network > Virtual Routers
Notes: The Ethernet interfaces and VLAN interfaces defined on the firewall receive and forward the Layer 3 traffic. The destination zone is derived from the outgoing interface based on the forwarding criteria, and policy rules are consulted to identify the security policies to be applied.
In addition to routing to other network devices, virtual routers can route to other virtual routers within the same firewall if a next hop is specified to point to another virtual router.

## Slide 31: Summary
You have learnt about firewalls:
Firewall Deployment Options
Virtual Wire Interface
Layer 3 Interface
  Security Zone
  Interface Management Profile
  DHCP
  Virtual Router